## Slide 1
K2BSA
2013 National Jamboree
Radio
Merit Badge

## Slide 2: Radio Merit Badge
K2BSA
Class Sessions
2013 National Jamboree
Session 1 – Radio basics, safety, and amateur radio
Session 2 – Amateur radio operating experience
Session 3 – Electromagnetic spectrum, components, careers, amateur radio licensing, and emergencies

## Slide 3: Radio Merit Badge
K2BSA
Class Sessions
2013 National Jamboree
Session 1 – Radio basics, safety, and amateur radio

## Slide 4: Radio
K2BSA
What is Radio
2013 National Jamboree
Radio M.B Req. 1
Radio is a way to electronically communicate from one place to another without wires
Radio is used in broadcasting, two way radios, television, mobile telephones, wireless LANs, garage door openers, car locks, EZpass, satellites, pagers, radar, microwave ovens, etc.

## Slide 5
K2BSA
Broadcast Radio and
Hobby Radio
2013 National Jamboree
The differences between Broadcast & Hobby Radio
Broadcast radio sends information to many people at the same time.
  Examples: talk radio, music, or television.
Radio M.B Req. 1a
Hobby Radio is used by amateur radio & citizens band operators and people that engage in activities where radio is helpful
  Examples: controlling models or tracking balloons or Family Radio Service (FRS) radios when camping

## Slide 6
K2BSA
Broadcast Radio and
Hobby Radio
2013 National Jamboree
Differences between Broadcasting & Two-Way Radio
Broadcasting is one-way communication from a transmitter to many receivers. It is usually planned programming and may be commercial with music, news, sports and advertising or non-commercial from schools, community radio stations, or National Public Radio (NPR).
Radio M.B Req. 1a
Two-way radio uses both a transmitter and receiver at both ends. Examples are walkie-talkies, amateur radio, mobile telephones, fire and police, taxis, aviation, ships, military, etc.

## Slide 7: Radio Station Call Signs
K2BSA
Radio Call Signs
2013 National Jamboree
Call signs are a unique identification for a licensed radio station.
Broadcast radio station call signs are three or four letters.
  WABC, WLS, KNBC, KCMO
U.S. Amateur radio station call signs are letters and a number beginning with W, K, A, or N.
  W1AW, K9BR, KB3BOY, WW9Y, N3YVH, K2BSA
Create Your Imaginary Call Sign
  Pick K, N, or W, a number, and add your initials
Radio M.B Req. 1.c.

## Slide 8
K2BSA
Radio Call Signs
2013 National Jamboree
K
PREFIX
BSA
SUFFIX
K2BSA
PREFIX
NUMBER
SUFF
IX
W, K, N, A – USA F – France
VE, VO, XJ – Canada I – Italy
XE – Mexico 4X, 4Z – Israel
PY – Brazil JA – Japan
G – Great Britain ZL – New Zealand
2
ORIGINAL
CALL SIGN
DISTRICT
KL7
KH6
7
6
5
O
4
9
8
3
2
1
Radio M.B Req. 1.c

## Slide 9
K2BSA
Radio Call Signs
2013 National Jamboree
N1RY = “1 X 2”
K7S = “1 X 1”
(SPECIAL EVENT STATION)
NK8W = “2 X 1”
AE5BT = “2 X 2”
K2BSA = “1 X 3”
KD4MML = “2 X 3”
Radio M.B Req. 1.c

## Slide 10: Phonetic Alphabet
K2BSA
Phonetic Alphabet
2013 National Jamboree
Many letters sound similar.
Over the radio, the letter C, E, V or Z might sound the same.
Weak radio signals and noise might make it difficult to hear voices.
An operator for whom English is not a native language may alter letter pronunciation.
Radio M.B Req. 1.d.
Radio operators use a phonetic alphabet to improve understanding and avoid communication errors.

## Slide 11: Phonetic Alphabet
K2BSA
Phonetic Alphabet
2013 National Jamboree
Alfa (AL FAH)
Bravo (BRA VOH)
Charlie (CHAR LEE)
Delta (DELL TAH)
Echo (ECK OH)
Foxtrot (FOKS TROT)
Golf (GOLF)
Hotel (HOH TELL)
India (IN DEE AH)
Juliette (JEW LEE ETT)
Kilo (KEY LOH)
Lima (LEE MAH)
Mike (MIKE)
November (NO VEM BER)
Oscar (OSS CAH)
Papa (PAH PAH)
Quebec (KEH BECK)
Romeo (ROW ME OH)
Sierra (SEE AIR RAH)
Tango (TANG OH)
Uniform (YOU NEE FORM)
Victor (VIK TAH)
Whiskey (WISS KEY)
X-ray (ECKS RAY)
Yankee (YANG KEY)
Zulu (ZOO LOO)
Radio M.B Req. 1.d.

## Slide 12
A
B
Earth
K2BSA
How Radio Waves Travel
2013 National Jamboree
Earth
Radio M.B Req. 2.a.
Local
Around the World
Ionosphere

## Slide 13
K2BSA
How Radio Waves Travel
2013 National Jamboree
Radio M.B Req. 2.a.
Drawing from WØSTU

## Slide 14: How High Frequency (HF) Radio Waves Travel
K2BSA
How Radio Waves Travel
2013 National Jamboree
Radio M.B Req. 2.a.
Ionosphere
Ground Wave (Local)
Sky Wave (DX)
Skip
Local
DX
Ionosphere
Earth
Skip

## Slide 15: WWV and WWVH
K2BSA
WWV and WWVH
2013 National Jamboree
Radio M.B Req. 2.a.
National Bureau of Standard radio stations that provide accurate frequencies, time, and HF propagation forecasts.
WWV & WWVH transmit on 2.5, 5, 10, 15 and 20 MHz.
WWV is in Ft Collins, Colorado and WWVH is in Kauai, Hawaii.
Listening to WWV or WWVH provides an indication of the radio frequencies that are being reflected from the ionosphere and the locations from which you may hear radio stations for each frequency.

## Slide 16
WWVH
Hawaii
WWV
Colorado
Earth
K2BSA
WWV and WWVH
2013 National Jamboree
Radio M.B Req. 2.a.
SBR W.Va.
Ionosphere
Sky waves skip around the world.

## Slide 17: WWV in Ft. Collins, CO
K2BSA
WWV and WWVH
2013 National Jamboree
Radio M.B Req. 2.a.

## Slide 18: WWV and WWVH
K2BSA
WWV and WWVH
2013 National Jamboree
Radio M.B Req. 2.a.

## Slide 19: DX and Local Stations
K2BSA
DX and Local
2013 National Jamboree
Radio M.B Req. 2.b.
A DX station is a distant station usually located in another country.
  DX is the old Morse code abbreviation for distance. It refers to hearing or communicating with a radio station that is far away.
A local radio station is located in the nearby community or region.

## Slide 20: FCC – Federal Communications Commission
K2BSA
ITU and FCC
2013 National Jamboree
Radio M.B Req. 2.b.
The FCC sets and enforces technical standards for devices that produce radio frequencies and issues licenses for radio stations, transmitters and operators.
The FCC does not have any authority outside of the United States.

## Slide 21: ITU – International Telecommunications Union
K2BSA
ITU and FCC
2013 National Jamboree
Radio M.B Req. 2.b.
The ITU coordinates global telecommunications networks and services including management of radio frequency spectrum and satellite orbits.
The ITU tries to prevent harmful interference between radio stations but it depends upon cooperation among countries as it does not have the ability to enforce actions.

## Slide 22
K2BSA
Block Diagram vs Schematic
2013 National Jamboree
Pippin QRP TX
G3MY
R1
68K
R2
56
R3
560
C2
50pf
C3
150pf
C1
56pf
XTAL
80m
Q1
2N2222A
Q2
2N3905
RFC1
22uh
C4
0.1uf
C5
100nf
L1
L2
C6
C7
C8
+12 to 14
VDC
>1 watt
50 ohm
KEY
Oscillator
Amplifier
Radio M.B Req. 5a
Simple Block Diagram
A block diagram shows a system as a
series of connected boxes.
Schematic Diagram
A schematic diagram of an electrical circuit is a drawing that shows how the circuit is built.

## Slide 23
K2BSA
Detailed Block Diagrams
2013 National Jamboree
Radio M.B Req. 5.a.
Shows more about how radios work

## Slide 24
K2BSA
Detailed Schematic Diagram
2013 National Jamboree
Radio M.B Req. 5.a.
Shows how to build a radio from components

## Slide 25
K2BSA
Block Diagrams
National Jamboree
Radio M.B Req. 5 b
Draw a block diagram of a radio station:
ANTENNA
TRANSCEIVER
AMPLIFIER
FEED
LINE
Microphone
Speaker

## Slide 26
K2BSA
Block Diagrams
National Jamboree
TRANSCEIVER
AMPLIFIER
ANTENNA
FEED
LINE
Microphone
Radio M.B Req. 5 b
Draw a block diagram of a radio station:

## Slide 27: Safety
K2BSA
Safety
National Jamboree
Radio M.B Req. 5 b

## Slide 28: Electricity Safety
K2BSA
Electricity Safety
2013 National Jamboree
Electricity can kill you.
Minimum fatal voltage – 30 volts.
Minimum fatal current if passed through the human heart – 1/10th of an ampere.
Power lines are often suspended in the air and not insulated.
Power lines carry thousands of volts – never touch them.
Radio M.B Req. 6

## Slide 29: Radio Safety Precautions
K2BSA
Radio Safety
2013 National Jamboree
Unplug equipment before working on it.
Never let anyone turn the power on and off for you.
Don’t work on a radio when you are tired.
Don’t use your bare hands to adjust components.
Don’t let your body be a ground path by touching grounded metal or standing in water.
Never wear headphones while working on a radio.
“Keep one hand in your pocket” so electricity can’t travel through your chest.
Tell your family how to turn off the power.
Be careful; death is permanent.
Radio M.B Req. 1.c.

## Slide 30: Radio Frequency (RF) Energy
K2BSA
RF Energy
2013 National Jamboree
Exposure to high levels of radio frequency (RF) energy can be unhealthy. Direct contact can cause burns; human eyes are sensitive to RF energy.
Don't use a radio when it is not completely assembled as the cabinet shields the RF radiation.
Keep antennas out of reach.
Radio M.B Req. 1.c.

## Slide 31
K2BSA
Grounding
National Jamboree
Direct Current
Circuit Grounding
“Grounding” means establishing an electrical connection to an “electrically neutral” object that is at “0” Volts electric potential.
  A “ground” is often a long metal rod driven into the earth.
  Grounding is a safety measure to prevent electric shock and equipment damage.
Radio M.B Req. 6
Direct Current Circuits in radio equipment are grounded to prevent electric shock. The circuit is connected to the metal cabinet or “chassis” and the chassis is connected to a ground.

## Slide 32
K2BSA
Grounding
National Jamboree
Power Outlet Grounding
Electric power enters a house through a box of circuit breakers. A metal ground rod is driven into the earth near where power enters the house to establish a Ground.
Radio M.B Req. 6
Power Outlets are connected to the circuit breaker box with three wire cable and one of the wires is connected to Ground.
Equipment is connected to Power Outlets with three prong plugs and one prong is connected to the Ground.
  The equipment case is then grounded to prevent electric shock.

## Slide 33
K2BSA
Grounding
National Jamboree
Antenna System Grounding
Antenna systems often include tall towers or objects that might be struck by lightning.
Antenna systems include transmission lines connecting the antenna to radio equipment.
Lightning arrestors are devices inserted into transmission line with a spark gap or gaseous discharge to ground.
Radio M.B Req. 6
Antenna system grounding should include both a ground connection for the antenna tower and a lightning arrestor in the transmission line where it enters the house.
The lightning arrestor may discharge static electricity but likely offers little protection from a direct strike.

## Slide 34
K2BSA
Antennas and Towers
National Jamboree
Antennas and Towers
Never install an antenna over, under, or very near a power line.
Avoid the possibility of the antenna falling on the power line or the power line falling on the antenna.
Radio M.B Req. 6

## Slide 35
K2BSA
Antennas and Towers
National Jamboree
Antennas and Towers
Never install an antenna where a person could touch the antenna.
Be careful working on towers and roofs.
  Protect yourself from falling.
  Protect people below you from falling objects.
  Use safety harnesses, belts, tethers, and hard-hats.
Radio M.B Req. 6

## Slide 36
K2BSA
Lightning Protection
National Jamboree
Lightning Protection
Antenna support poles and towers should be connected to a ground rod.
Disconnect radios if lightning is in the area.
Lightning could strike your antenna and travel down the transmission line to the radio.
Make sure your antenna and radio are grounded to a good earth ground.
Never operate your radio in thunderstorms.
Radio M.B Req. 6

## Slide 37: Amateur Radio
K2BSA
Amateur Radio
National Jamboree

## Slide 38
K2BSA
Amateur Radio Service
National Jamboree
What is Amateur Radio?
Radio M.B Req. 9.a(1)
A type of two-way radio. A place to learn about radio.
Called the “Amateur Radio Service” because it can’t be used for profit.
Also known as “Ham Radio”.
An important part of disaster response.
A lot of fun!

## Slide 39
K2BSA
Amateur Radio Service
National Jamboree
Why does the FCC have an
Amateur Radio Service?
Radio M.B Req. 9.a(1)
Public service - community service and disaster help (A Scout does a good turn daily – here is another way).
International goodwill - A great way to talk to people in other countries.
Experimentation - Hams have made inventions like FM, SSB, Packet Radio, Automatic Position Reporting Systems.
Communication skills - Many people trained to communicate.

## Slide 40: Amateur Radio Activities
K2BSA
Amateur Radio Service
National Jamboree
Radio M.B Req. 9.a(1)
Jamboree On The Air (JOTA)
  The third weekend every October.
  Scouts all over the world talk to each other on ham radio. Largest annual scouting event.
DX (Long Distance Communication)
  Talk to other hams around the world.
  Collect QSL cards (postcards) to prove contact (Collect countries!).
  Great way to have fun and learn geography.
Contests
  Held many weekends to contact as many people as possible from a certain place or in a certain way.

## Slide 41
K2BSA
Amateur Radio Service
National Jamboree
Amateur Radio Activities
Radio M.B Req. 9.a(1)
Skywarn
  National Weather Service uses Hams to
  report severe weather
“Fox” hunting (Radio Direction Finding)
  Hidden transmitters
  Tagged wildlife
  Downed aircraft
  Life rafts
  Stolen cars
Packet radio
  Sending electronic messages (e-mail, text) via radio

## Slide 42
K2BSA
Amateur Radio Service
National Jamboree
Amateur Radio Activities
Radio M.B Req. 9.a(1)
Public Service.
  Parades & special events from small carnivals to the Rose Bowl Parade.
  Help with communication at large community events, marathons, bike-a-thons, etc.

## Slide 43
K2BSA
Amateur Radio Service
National Jamboree
Amateur Radio Activities
Radio M.B Req. 9.a(1)
Disaster Communication
  Hams help during fires, floods, earthquakes, and other disasters.
  At these times, telephone lines and cell phone sites are often damaged or overloaded.
  Ham radio is the only reliable form of communication.

## Slide 44
K2BSA
Amateur Activities
National Jamboree
Foxhunting
Bicycle Station
OSCAR
Radio M.B Req. 9a(1)
Morse Code

## Slide 45
K2BSA
Amateur Activities
National Jamboree
Kit Building
Mobile
Moonbounce
Radio M.B Req. 9a(1)

## Slide 46
K2BSA
Amateur Activities
National Jamboree
Digital Modes
Slow Scan TV image from MIR
Emergency
Communications
Field Operating
Radio M.B Req. 9a(1)

## Slide 47
K2BSA
Q Signals and Abbreviations
National Jamboree
QRM | Interference (Your radio signal is being interfered with.)
QRN | Static (Your radio signal is being interfered with by static.)
QRP | Low power radio operation
QRS | Send your Morse code more slowly.
QRT | Leaving the air (I’m stopping my radio activity.)
QRX | Wait a few minutes.
QRZ? | Who is calling?
QSB | Your signals are fading.
QSL | A card sent to indicate you’ve talked to or heard a radio station; also, as a Q signal that means (Received OK)
QSO | A conversation.
QSY | I am moving to another radio frequency. . .
QTH | My location is. . .
73 | Best regards
RST | Readability, Strength, Tone (Signal report)
CQ | I am calling…
Radio M.B Req. 9a(2)

## Slide 48: Radio Merit Badge
K2BSA
Class Sessions
2013 National Jamboree
Session 2 – Amateur radio operating experience

## Slide 49: Make a Ham Radio Contact
K2BSA
Radio Operations
2013 National Jamboree
Listen and call another ham radio station
Talk with the other Radio Station Operator.
  Relax and have fun
  Your name
  Where you live
  Describe your school
  Talk about Scout camp
Use Q-signals
Log your contact

## Slide 50: Log Your Contact
K2BSA
Radio Operations
2013 National Jamboree
His Name ________________
His Call ________________
His QTH (location) ________________
Frequency ________________
Mode ________________
His RST (signal report) ________________
My RST (signal report) ________________
Comments ________________

## Slide 51: Radio Merit Badge
K2BSA
Class Sessions
2013 National Jamboree
Session 3 – Electromagnetic spectrum, components, careers, amateur radio licensing, and emergencies

## Slide 52
K2BSA
Q Signals and Abbreviations
National Jamboree
QRM | Interference (Your radio signal is being interfered with.)
QRN | Static (Your radio signal is being interfered with by static.)
QRP | Low power radio operation
QRS | Send your Morse code more slowly.
QRT | Leaving the air (I’m stopping my radio activity.)
QRX | Wait a few minutes.
QRZ? | Who is calling?
QSB | Your signals are fading.
QSL | A card sent to indicate you’ve talked to or heard a radio station; also, as a Q signal that means (Received OK)
QSO | A conversation.
QSY | I am moving to another radio frequency. . .
QTH | My location is. . .
73 | Best regards
RST | Readability, Strength, Tone (Signal report)
CQ | I am calling…
Radio M.B Req. 9a(2)

## Slide 53: The Electromagnetic Spectrum
K2BSA
2013 National Jamboree

## Slide 54: Radio Waves
K2BSA
Electromagnetic Spectrum
2013 National Jamboree
Radio M.B Req. 3.a.
Electromagnetic energy
Travels at the speed of light

## Slide 55: Radio Waves
K2BSA
Electromagnetic Spectrum
2013 National Jamboree
Radio M.B Req. 3.a.

## Slide 56: Frequencies (One Hertz is one cycle per second)
K2BSA
Electromagnetic Spectrum
2013 National Jamboree
Radio M.B Req. 3.a.
Direct Current ………0 Hertz (goes in only one direction)
Alternating Current ..60 Hertz (Hz)
Audio (Sound)………100 Hz to 20 kHz (100-20,000 Hz)
LF…………………….30-300 kHz (30,000-300,000 Hz)
MF……………………0.3-3 MHz (300,000-3,000,000 Hz)
HF or Shortwave……3-30 MHz (3,000,000-30,000,000 Hz)
VHF ………………….30-300 MHz (30,000,000-300,000,000 Hz)
UHF………………….300-3,000 MHz (well, you get the idea)
Microwave…………..Frequencies above 500 MHz
Visible Light………...400-800 THz (400,000,000-800,000,000 MHz)

## Slide 57: The Electromagnetic Spectrum
K2BSA
Electromagnetic Spectrum
2013 National Jamboree
Radio M.B Req. 3.a.
Sound
Long Radio Wavelengths
Short Radio Wavelengths
Microwaves
Frequency - Measured in Hertz (kilohertz, megahertz, gigahertz)
Wavelength – Measured in meters (cm)
Inverse relationship between frequency and wavelength
Notes: Different frequencies in the Electromagnetic spectrum are used for different purposes and travel a bit differently.
Medium Frequencies - The frequencies from 300 KHz to 3 MHz are called the Medium Frequencies. The usually follow the earth's surface using "Ground Waves" and can reach hundreds of miles. AM broadcasters are found here
High Frequencies - The frequencies from 3 MHz to 30 MHz are called the High Frequencies or "HF" The usually bounce off the Ionospere using "Sky Waves" and can reach thousands of miles. Shortwave broadcasters and many Ham bands are found here
Very High Frequencies - The frequencies from 30 MHz to 300 MHz are called the Very High Frequencies or "VHF" The usually go right through the Ionospere and so are mostly used for line of sight communications on earth. They also can be used to talk to spacecraft. FM Radio and TV broadcasters as well as many Police, Fire and Aircraft radios operate here. The popular 6 meter and 2 meter Ham bands are found here.
Ultra High Frequencies - The frequencies from 300 MHz to 3000 MHz are called the Ultra High Frequencies or "UHF" The usually go right through the Ionospere and so are used for line of sight communications on earth. They also can be used to talk to spacecraft. UHF TV broadcasters as well as some Police, Fire radios and cell phones operate here. The 440 MHz Ham band is found here.

## Slide 58
300 kHz
500 kHz
1.64 MHz
1.8 MHz
3 MHz
3 MHz
10 MHz
15 MHz
20 MHz
30 MHz
Medium Frequencies (MF) – 300 kHz to 3 MHz
High Frequencies (HF) – 3 MHz to 30 MHz
Very High Frequencies (VHF) – 30 MHz to 300 MHz
Ultra High Frequencies (UHF) – 300 MHz to 3000 MHz
30 MHz
50 MHz
88 MHz
108 MHz
144 MHz
220 MHz
300 MHz
300 MHz
1000 MHz
2000 MHz
3000 MHz
Chart adapted from WØSTU

## Slide 59
Medium Frequencies (MF) – 300 kHz to 3 MHz
High Frequencies (HF) – 3 MHz to 30 MHz
Very High Frequencies (VHF) – 30 MHz to 300 MHz
Ultra High Frequencies (UHF) – 300 MHz to 3000 MHz
K2BSA
Electromagnetic Spectrum
2013 National Jamboree
300 kHz 500 kHz 1640kHz 1800kHz 3 MHz
AM Broadcast
160m Ham
3 MHz 10 MHz 15 MHz 20 MHz 25 MHz 30 MHz
30m Ham
80m Ham
40m Ham
20m Ham
15m Ham
12m Ham
10m Ham
30 MHz 88 MHz 108MHz 144 MHz 220 MHz 300 MHz
300 MHz 1000 MHz 2000 MHz 3000 MHz
FM
2m Ham
TV
Ham
6m Ham
TV
Ham
TV
Ham
Ham
CB
Aviation
Aviation
Aviation
Aviation

## Slide 60: Frequency Assignments
K2BSA
Electromagnetic Spectrum
2013 National Jamboree
Radio M.B Req. 3.a.
AM Broadcast Radio
FM Broadcast Radio
Short Wave Broadcast
Television Broadcast
CB Radio
Police Radio
Amateur Radio
Mobile Telephone
Wi-Fi
540 - 1600 kHz
88 - 108 MHz
5 - 22 MHz
Channel 2 = 54-60 MHz
27 MHz
450-470 MHz
3.5, 7, 10, 14, 21, 28, 50, 144 MHz
80, 40, 30, 20, 15, 10, 6, 2 meters
850 - 900 MHz, 1800 – 1900 MHz
2400 – 2470 MHz

## Slide 61: How Radio Waves Carry Information
K2BSA
How Radio Waves
Carry Information
2013 National Jamboree
Radio M.B Req. 4
A pure radio wave does not convey information.
Radio waves carry information when they are changed by a process called modulation.
Modulation
  Continuous wave (CW)
  Amplitude (AM)
  Frequency (FM)

## Slide 62
K2BSA
How Radio Waves
Carry Information
2013 National Jamboree
Radio signals are modulated(changed) with information.
  Morse Code uses dots and dashes
  Voice, images – AM, FM, TV
  Digital modes – 1s and 0s
Radio M.B Req. 4

## Slide 63: Continuous Wave (CW) The Oldest Digital Mode
K2BSA
How Radio Waves
Carry Information
2013 National Jamboree
Radio M.B Req. 4
Works by simply turning the transmitter
on and off in a pattern called Morse Code

## Slide 64: “CW” or Morse Code
K2BSA
How Radio Waves
Carry Information
2013 National Jamboree
Radio M.B Req. 4

## Slide 65: Modulation
K2BSA
How Radio Waves
Carry Information
2013 National Jamboree
Radio M.B Req. 4
FM
AM
PM

## Slide 66
K2BSA
How Radio Waves
Carry Information
2013 National Jamboree
Basic Radio Equipment
  A Transmitter sends radio signals using
  modulation to convey information.
  A Receiver converts (demodulates) very weak radio signals into audio.
Radio M.B Req. 4

## Slide 67
K2BSA
How Radio Waves
Carry Information
2013 National Jamboree
Basic Radio Equipment
  A Transceiver combines the transmitter and receiver in one unit.
  An Amplifier increases the strength of the radio wave produced by the transmitter.
  The Antenna sends radio signals out into the air and captures received radio signals.
Radio M.B Req. 4
Transceivers
Antenna

## Slide 68
K2BSA
How Radio Waves
Carry Information
2013 National Jamboree
Radio M.B Req. 4
TRANSMITTER
AMPLIFIER
ANTENNA
FEED
LINE
KEY
MIC
T-R
SWITCH
RECEIVER
Speaker
Radio Station Block Diagram

## Slide 69
K2BSA
How Radio Waves
Carry Information
2013 National Jamboree
Radio M.B Req. 4
TRANSCEIVER
AMPLIFIER
ANTENNA
FEED
LINE
KEY
MIC
Speaker
Radio Station Block Diagram

## Slide 70
K2BSA
Circuits
National Jamboree
+
-
Flashlight
Radio M.B Req. 5c
An open circuit exists when the path for electricity is incomplete as when the flashlight switch is off.
Open Circuit
Off
On

## Slide 71
K2BSA
Circuits
National Jamboree
Flashlight
Radio M.B Req. 5c
A closed circuit exists when the path for electricity is complete as when the flashlight switch is on.
Closed Circuit
Off
+
-
On

## Slide 72
K2BSA
Circuits
National Jamboree
Flashlight
Radio M.B Req. 5c
A short circuit exists when the path for electricity is completed in an unplanned way like when a tool “shorts” the circuit.
Short Circuit
Off
On
+
-

## Slide 73
K2BSA
Schematic Symbols
National Jamboree
Radio M.B Req. 5d
Resistor
Diode
Variable Capacitor
Capacitor
Draw Schematic Symbols

## Slide 74: Draw Schematic Diagrams
K2BSA
Schematic Symbols
National Jamboree
Radio M.B Req. 5d
Integrated Circuit
Transistor
Inductor
Switch

## Slide 75: Describe Your K2BSA Visit
K2BSA
Visit K2BSA
2013 National Jamboree
Radio M.B Req. 7
What equipment did you see?
How was the equipment used?
What licenses are required to operate and maintain the equipment?
What is the purpose of the radio station?

## Slide 76: Radio Careers
K2BSA
Radio Careers
2013 National Jamboree
Radio M.B Req. 8
Technical Careers
Broadcasting Careers
Operator Careers

## Slide 77: Technical Radio Careers
K2BSA
Radio Careers
2013 National Jamboree
Radio M.B Req. 8
A Design Engineer develops the block diagrams and schematics to create a radio.
A Design Technician selects the actual parts and determines the physical arrangement of those parts on the printed circuit board.
A Manufacturing Engineer determines how to purchase the parts and assemble the radio.
A Radio Station Engineer operates and maintains the radio station equipment.
An Electronics Technician repairs radio equipment.

## Slide 78: Broadcasting Careers
K2BSA
Radio Careers
2013 National Jamboree
Radio M.B Req. 8
Announcers and Radio/TV Personalities perform the on-the-air communication at a radio or TV station.
The Station Manager is responsible for the overall operation of the radio or TV station.
The Program Director or Music Director will be responsible for the content of the broadcast material.
A Program Writer will be responsible for producing for some programs the actual text read by the Announcers or Personalities.

## Slide 79: Radio Operator Careers
K2BSA
Radio Careers
2013 National Jamboree
Radio M.B Req. 8
Radio communication systems are everywhere in our culture.
Many careers include radio operation incidental to the main career role. For example, radio communication is essential for policemen to function effectively.
All public safety functions like fire and ambulance services require radio communication operations.
Aviation traffic management relies on very extensive radio communication networks.
Military operations rely upon radio networks.

## Slide 80: Education for Radio Careers
K2BSA
Radio Careers
2013 National Jamboree
Radio M.B Req. 8
Most jobs require high school diploma.
Radio engineers generally study electrical engineering at college.
Colleges offer courses in broadcasting and communications.
Gain broadcasting experience at college radio stations.
Radio technicians attend trade schools or community colleges.
Many organizations offer radio license training courses and certifications.

## Slide 81: Amateur Radio Licenses
K2BSA
Amateur Radio Licenses
National Jamboree
Radio M.B Req. 9.a.(4)
Technician Class
  Elementary operating procedures.
  Radio regulations.
  Beginning electronics.
  Emphasis on VHF and UHF.
General Class
  Intermediate practices, regulations, theory.
  Operating privileges in all amateur bands with some limits on frequencies.
  Emphasis on HF.
Amateur Extra Class
  Advanced theory and practices.
  All operating privileges in all bands.
  Administer license exams.

## Slide 82: Technician Class License
K2BSA
Amateur Radio Licenses
National Jamboree
Radio M.B Req. 9.a.(4)
No age restriction
Elementary operating procedures
Radio regulations
Beginning electronics
Emphasis on VHF and UHF
35-question, multiple-choice written examination
Minimum passing score is 26 correct answers – 74%

## Slide 83: Amateur Radio License Exams
K2BSA
Amateur Radio Licenses
2013 National Jamboree
Radio M.B Req. 9.a.(4)
Amateur radio license exams are given by Hams called “Volunteer Examiners”
Exams and free study classes are given by local radio clubs
More information about ham radio can be found at the ARRL web page: www.arrl.org

## Slide 84: Emergency Calls
K2BSA
Emergency Calls
National Jamboree
Radio M.B Req. 9.a.(5)
You may use any radio at any time to get help during an emergency.
“Break” “Break” followed by your call sign to interrupt a radio conversation in progress.
“MAYDAY” is the international word for requesting help by radio – “EMERGENCY” also works.
Speak clearly and give a complete location and information like a 911 call.
You might have to climb higher up a hill with an FRS radio or cell phone.
In Morse code you would slowly send SOS (   ─ ─ ─   ) and give the same information.

## Slide 85: Radio Station Types
K2BSA
Handhelds, Base, Mobile
National Jamboree
Radio M.B Req. 9.a.(6)
Handheld radios (HT): Small, light, portable, but not much power Some can fit in your pocket. With repeaters they can be quite useful and they can easily be carried on a hike.
Base station radios: Permanent station in a building. More power, easier to use, more features.
Mobile radios: Permanent station in a vehicle. More power.
Which kind of radio is best? It depends on what you want to do.

## Slide 86: Repeaters
K2BSA
Handhelds, Base, Mobile
National Jamboree
Radio M.B Req. 9.a.(6)
Repeaters are transceivers located on high points (Mountains, tall buildings, satellites) to automatically relay radio signals. Some have connections to the telephone system.
A repeater receive on one frequency and re-transmits on another.
A repeater extends the range of a handheld transceiver.

## Slide 87: VHF Propagation with Repeaters
K2BSA
Handhelds, Base, Mobile
National Jamboree
Radio M.B Req. 9.a.(6)

## Slide 88
K2BSA
2013 National Jamboree
Radio
Merit Badge